## Slide 1: A hierarchical, NSI compatible, topology proposal for NML

## Slide 2: Why a hierarchical topology?
The existing NSI topology model does not provide a consistent mechanism for exposing intra-domain topological structure.
  The base model hides all internal structure…which is good in many cases…. But…
  Where a network wishes to do so, it should be able to expose additional internal structure or state in a measured and graduated degree…down to the hardware minutia if desired.

## Slide 3: NML recommendations
This proposal retains the NSI abstractions at the highest topological layer,
and retains the NSI model internally as smaller NSI domains are defined
A key relation called an “alias” is defined to link STPs (NML Ports) at a particular level to STPs at the next lower (more detailed) level.
  An Alias is an internal topological construct that is stored at the lower level (more detailed level). It therefore stays private until/unless that level is announced externally.
An Alias may reference a conventional NML topological object – thus mapping the NSI construct to the corresponding NML object as the local topology manager deems appropriate.

## Slide 4: NSI Topology Example Current existing NSI topology model: only L0 has structure, L1+ is opaque
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Opaque internal
Topo level 1
Universal space
Topo level 0
Pionier-i
NetherLight-i
NetherLight-o
Internet2-i
Internet2-o
Pionier-o
ION-o
NDNi
NDNo
NDNi
NDNo
NDNi
NDNo
SDPs (NML Links)
STPs (NML Ports)

## Slide 5: Proposed Hierarchical NSI Topology Example Proposed NorthernLight topology: L0 & internal L1 objects are publically announced by NorthernLight; As a Worldview, this topo would say I2, PSNC, and NL only announced L0 information. As a Local Topology from NDN, this is the only L0 information that NorthernLight can provide (i.e. its direct adjacencies)
PSNC
Topo level 1
NetherLight
Topo level 1
Internet2
Topo level 1
NDN.EFDX
Topo level 1
Universal space
Topo level 0
NYC Level 2
CPH
Level 2
Pionier-i
NetherLight-i
NetherLight-o
Internet2-i
Internet2-o
Pionier-o
ION-o
AMSi
POZi
NYCi
NYCo
AMSo
POZo
NDNi
NDNo
CPHo
CPHi
IONo
IONi
NDNi
NDNo
NDNi
NDNo
Blue links are “aliases” indicating an external level transition in the topology

## Slide 6: Hierarchical NSI Topology Example World view from a NorthernLight “internal” path perspective
NDN.EFDX
Topo level 1
All internal
NYC Level 2
CPH
Level 2
Pionier-i
Internet2-i
Internet2-o
Pionier-o
AMSi
POZi
NYCi
NYCo
AMSo
POZo
CPHo
CPHi
IONo
IONi
Level 0
All external

## Slide 7: Hierarchical Topology Proposal Example
topo{ name $L0$; /* level 0 is the universal space */
topo{ name NDN.EFDX; /* level 1 topology */
NSA https://orval.grid.aau.dk:9443/NSI/services/ConnectionService
port Pionier-i, NetherLight-i, Internet2-i inbound;
port Pionier-o, NetherLight-o, Internet2-o outbound;
topo{ name CPH; location lat 24.1234 lon -57.2345; /* level 2 topology */
port AMSi, POZi, NYCi inbound;
port AMSo, POZo, NYCo outbount;
}
topo{ name NYC; location lat 24.1234 lon -87.2345; /* level 2 topology */
port IONi, CPHi inbound;
port IONo, CPHo outbount;
}
link NYC:CPHi, CPH:NYCo; /* level 2 to level 2 */
link NYC:CPHo, CPH:NYCi; /* level 2 to level 2 */
alias NDN.EFDX:Pionier-i, CPH:POZi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Pionier-o, CPH:POZo; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight-i, CPH:AMSi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:NetherLight-o, CPH:AMSo; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2-i, NYC:IONi; /* level 1 to level 2 boundary links */
alias NDN.EFDX:Internet2-o, NYC:IONo; /* level 1 to level 2 boundary links */
}
Link NDN.EFDX:Pionier-i, Pionier.EFDX:NDNo; /* NDN level 1 port to Pionier level 1 port *
Link NDN.EFDX:Pionier-o, Pionier.EFDX:NDNi;
Link NDN.EFDX:NetherLight-i, NetherLight.EFDX:NDNo; /* level 1 port to level 1 port */
Link NDN.EFDX:NetherLight-o, NetherLight.EFDX:NDNi;
Link NDN.EFDX:Internet2-i, Internet2.EFDX:NDNo; /* level 1 port to level 1 port */
Link NDN.EFDX:Internet2-o, Internet2.EFDX:NDNi;
}

## Slide 8: Merging topologies
Intelligent semantic analysis of topology descriptions is necessary when merging two topologies:
  E.g. “link aruba:a1, bonaire:b1” is equivalent to “link bonaire:b1, aruba:a1”
  E.g. “port a1, a2, a3 inbound;” is equivalent to “port a1 inbound; port a3, a2 inbound;”
  E.g. “topo{ link a,b; topo{…}; }” is equivalent to “topo{ topo{…}; link a, b;}”