## Slide 1: Network Markup Language (NML)
OGF 40, Oxford

## Slide 2: OGF IPR Policies Apply
“I acknowledge that participation in this meeting is subject to the OGF Intellectual Property Policy.”
Intellectual Property Notices Note Well: All statements related to the activities of the OGF and addressed to the OGF are subject to all provisions of Appendix B of GFD-C.1, which grants to the OGF and its participants certain licenses and rights in such statements. Such statements include verbal statements in OGF meetings […]
Excerpt from Appendix B of GFD-C.1: ”Where the OGF knows of rights, or claimed rights, the OGF secretariat shall attempt to obtain from the claimant of such rights, a written assurance that upon approval by the GFSG of the relevant OGF document(s), any party will be able to obtain the right to implement, use and distribute the technology or works when implementing, using or distributing technology based upon the specific specification(s) under openly specified, reasonable, non-discriminatory terms. The working group or research group proposing the use of the technology with respect to which the proprietary rights are claimed may assist the OGF secretariat in this effort. The results of this procedure shall not affect advancement of document, except that the GFSG may defer approval where a delay may facilitate the obtaining of such assurances. The results will, however, be recorded by the OGF Secretariat, and made available. The GFSG may also direct that a summary of the results be included in any GFD published containing the specification.” “If you did read this, you accept a free drink from Freek”
Notes: IPR Notices Note Well for OGF meetings

## Slide 3: Agenda
NML base (proposed) changes
Identifiers
Future documents
Future of the NML-WG
NSI Topology Exchange (John & Chin)
NSI for a data center

## Slide 4: (Proposed) Changes in NML
OGF 40, Oxford

## Slide 5: Proposed Changes
Schema fixes for libxml2
Add labelType attribute to SwitchingService
Ports with different labels in a SwitchingService
AdaptationService between two PortGroups / SwitchingServices
Capacity, MTU, cost metric
Notes: NML base: GFD.206 (May 2013)

## Slide 6: Schema fixes for libxml2/xmllint
<xs:complexType name="SwitchingServiceType">
<xs:complexContent>
<xs:extension base="nml:NetworkObject">
<xs:sequence>
<xs:element name="Relation" type="nml:SwitchingServiceRelationType” minOccurs="0" maxOccurs="unbounded"/>
<xs:any namespace="##other" processContents="lax" minOccurs="0" maxOccurs="unbounded"/>
</xs:sequence>
<xs:attribute name="encoding" type="xs:anyURI" use="optional"/>
<xs:attribute name="labelSwapping" type="xs:boolean" use="optional"/>
<xs:attribute name="labelType" type="xs:anyURI" use="optional"/>
</xs:extension>
</xs:complexContent>
</xs:complexType>
Notes: What about ##local on the line before ##other?

## Slide 7: labelType attribute for SwitchingService
<xs:complexType name="SwitchingServiceType">
<xs:complexContent>
<xs:extension base="nml:NetworkObject">
<xs:sequence>
<xs:element name="Relation" type="nml:SwitchingServiceRelationType” minOccurs="0" maxOccurs="unbounded"/>
<xs:any namespace="##other" processContents="lax" minOccurs="0" maxOccurs="unbounded"/>
</xs:sequence>
<xs:attribute name="encoding" type="xs:anyURI" use="optional"/>
<xs:attribute name="labelSwapping" type="xs:boolean" use="optional"/>
<xs:attribute name="labelType" type="xs:anyURI" use="optional"/>
</xs:extension>
</xs:complexContent>
</xs:complexType>
Notes: Can this work with next proposed change?

## Slide 8: Different labelType in SwitchingService
encoding := frame format e.g. Ethernet, SDH, WDM)
labeltype := channel identifier type e.g. C-VLAN, S-VLAN, or I-SID for Ethernet e.g. K, L, M, or U label for SDH e.g. wavelength (CWDM), or frequency (DWDM) for WDM.
1:∞ relation between encoding:label

## Slide 9: Different labelType in SwitchingService
Example: Ethernet switch with tagged (802.1q label) and untagged (no label) Ports.
label-Swapping | Meaning
false | Both label and labeltype must match
true | All Ports can exchange data; no restriction with regard to label type or value

## Slide 10: AdaptationService
Now:
Port  AdaptationService  PortGroup
Proposed:
PortGroup  AdaptationService  PortGroup

## Slide 11: Capacity
Suggested, along with MTU and cost metric.
Not in NML-base. Perhaps in NML Ethernet extension.

## Slide 12: How to proceed?
Changes currently in nsi-wg-topology repository
https://redmine.ogf.org/projects/nsi-wg-topology/repository/revisions/master/show/schemas
Must be made into a NML 1.1 update
Volunteers after NSI-TS (NSI Topology Service) publication

## Slide 13: Identifiers: From Port ID to NSA URL
OGF 40, Oxford

## Slide 14: Outline
Heated discussion between Henrik, Jeroen and myself in Dec 2013.
Problem: how to get from a Port identifier to a Topology, and NSA*?
* The Network Service Agent, not your National Spying Atrocity
Notes: General; Previous; Current; Problem; NORDUnet proposal; Freek proposal; Topology Distribution; Future

## Slide 15: General
GFD.206 (NML-base): schema. Allows all URI as identifiers. not just urn:ogf:network:*.
GFD.202: defines urn:ogf:network identifiers: <PREFIX>:<ID-OF-ASSIGNING-ORG>:<LOCAL PART>
  <PREFIX> := 'urn:ogf:network’
  <ID-OF-ASSIGNING-ORG> := domain + ":" + date
Topology exchange not part of NML schema
NML is liberal NSI may need restrictions on NML

## Slide 16: Previously
STP := triplet (Topology ID, source PortGroup ID, sink PortGroup ID)
This works, but is not very pretty.
Problem: isAlias only points to a Port, not a Topology.

## Slide 17: Current
STP := single NML Port identifier
Triplet is not used anymore
Note: draft-gwdi-nsi-topology-service is not yet updated to reflect this change.
draft-gwdrp-nsi-topology-representation is up-to-date.

## Slide 18: Problem
How to get from a NML Port identifier to a Topology
How to get from a Topology to a NSA
Current solution: AutoGOLE is using a bootstrap file to make these mappings.
AutoGOLE solution does not scale, in particular if Topology and Port identifiers are in different namespaces. e.g.: Topology `http://some.example.org/our-network` hasOutboundPort Port `urn:ogf:network:other.example.net:2013:port-12345`

## Slide 19: NORDUnet Proposal
Port identifier must start with the Topology identifier
e.g.: Topology `urn:ogf:network:example.net:2013:network` Port `urn:ogf:network:example.net:2013:network:port-12345`
Solves Port  Topology mapping
Requires AutoGOLE bootstrap file, or Topology lookup service for Topology  NSA
Notes: By Lars Fischer and Henrik

## Slide 20: Knights-of-the-URNs Proposal
Only use urn:ogf:network identifiers
  This ensures a Port identifier  Prefix mapping
Solves Port  prefix mapping
Requires AutoGOLE bootstrap file, or Topology lookup service for prefix  NSA and prefix  Topology mapping
Notes: By Freek and Jeroen

## Slide 21: Knights-of-the-URNs Proposal
If and only if a strict Port ⟷ Topology mapping is necessary (besides the Port  prefix mapping):
Assigning organisation prefix of must be the same for Topology and the Ports it contains.
e.g.: Topology `urn:ogf:network:example.net:2013:network` Port `urn:ogf:network:example.net:2013:port-12345`
Considered better than e.g.: Topology `urn:ogf:network:example.net:2013:network` Port `urn:ogf:network:example.net:2013:network:port-12345`
Notes: By Freek and Jeroen

## Slide 22: Topology Distribution
from draft-gwdi-nsi-topology-service:
Centralized Manual Distribution
Version Controlled Distribution (AutoGOLE GitHub)
(PerfSonar) Lookup Service
HTTP Distribution (hop by hop traversal)
A Peer-to-Peer Distribution Protocol
Notes: ESnet has SLS = Simple Lookup Service
A Key-value store implemented using MongoDB.

## Slide 23: Future
Prefix  NSA mapping still needs to be solved
Freek thinks a lookup service is best solution
Jeroen (also) prefers a peer-to-peer solution
Handle system (lookup service) would have been perfect
If Freek would to things over, he'd have used the Handle system (DNS on steroids)
Handle and DNS: lookup service, root & delegation.
URN: lookup service defined (RFC 3402), not used
Simple Lookup Service by ESnet?
Notes: Handle: RFC 3651. Example: hdl.handle.net with or 10.5240/5868-409E-7BFB-536A-6067-E

## Slide 24: Intermezzo: The Handle System
RFC 6531, ISO 26324
General resolvers: hdl.handle.net, dx.doi.org
Identifier | Resolver | Resource
10.5240/5868-409E-7BFB-536A-6067-E | resolve.eidr.org | Movie database
10.1016/j.future.2006.03.007 | sciencedirect.com | Scientific publication
2333.1/v9s4mww5 |  | Files
10916/58405ca4-1f31-11e2-ba9d-14feb57d1255 | epic.sara.nl | Scientific data

## Slide 25: Future Documents
OGF 40, Oxford

## Slide 26: Future documents
NSI Topology Representation: Jeroen, John
Topology Distribution Mechanisms: Jeroen
Changes to NML-base: ?
Experience Document: ?
JSON syntax: Jeroen, Chin
Ethernet extensions: Jerry, Chin, Freek
IP extensions: –
Experimental Features: Freek, Henrik
OpenFlow extensions: waiting more experience

## Slide 27: Chair
Would appriciate candidates