## Slide 1: NSI Topology Thoughts on how topology fits into the NSI architecture
Jerry Sobieski
Feb 1,2010

## Slide 2: Basic NSI Topology
The NSI Architecture is intended to support a global network services model. Such a service architecture will require separate autonomous but cooperating domains in order to provide global scalability, flexability, security, and robustness.
  Distributed yet interoperable services necessarilly involve some notion of topology
The NSI Transport Topology Model is a simple directed graph model that provides both a suitable foundation for basic NSI service concepts (such as “tree” and “chain” pathfinding, service termination points, and user specified path constraints)
The simplicity of the NSI model also allows emerging notions of network federation, aggregation, topology summarization and abstraction, service definitions, and multi-layer/multi-domain service interoperability to be incorporated into the service layer.

## Slide 3: NSI Topology Model
The NSI Architecture assumes a “Node” based resource management model
  I.e. All resources are managed within Nodes by a Resource Manager agent.
The NSI topology identifies three basic elements:
Node := A vertex in the topology graph.
  A Node represents an opaque confluence point of one or more input Links and one or more output links
  A Node moves payload data from input port to output port, and may perform some function on the transport stream in the process. (e.g. segmentation/reassembly, CRC/Parity checks, etc.)
Port := An identifier that enumerates edges converging at a single vertex in the topology graph
  Within the context of a single Node, the Port id addresses the Links attached at that Node.
Link := An edge in the topology graph
  Links represent an atomic, unidirectonal, transparent, and static data transport connection between two ports

## Slide 4: Basic NSI Topology Element
I0
I1
In
O0
O1
Om
…
…
Node
Link
…
…
Link
Ports
A sample topology
Color elements are components of the NSI Topology
Node
Node
Link
Ports
End System

## Slide 5: NSI Topology Aggregation and Summarization
Complex physical topology
Multi-Domain aggregated/summarized topology
Equivalent NSI topology

## Slide 6: NSI Agent Relationships
A Resource Manager is an agent that allocates and manages network elements.
The RM may manage a group network elements connected together to form a single contiguous “domain”.
A domain is summarized and modeled as a single virtual network element whose internal topology or architecture is opaque to external agents
The RM is assumed to be authoritative for, and act on behalf of, all resources within the virtual node.
The NSA is the agent that interacts with NSAs representing other domains (virtual nodes) using the NSI Protocol.
Network Element
Resource Manager
Network Domain
Resource Manager

## Slide 7: NSI Agent Relationships
The Network Resource Manager communicates with other external Network Services Agents using the NSI Protocol.
The NRM is responsible for translating NSI protocol events and semantics into those internal actions necessary to implement the NSI functionality
Resource Manager
Network Service Agent
NSI Protocol
Allen
Bart
Chuck
To Peer
NSAs
To Aggregation NSAs
Requesting
Agents
Domain Bart
“super” Domain
Chuck
Domain Allen

## Slide 8: Channel Graph Representation (background on possibe topo ideas…)
Un-Directed Graph
Directed Graph
Node “A”
Element “C0”
Node “B”
A
B
C0
C1
Channel Graph
In the CG, all topo elements are treated as nodes (with ports), and the links in a CG
Indicate relationships between those topo elements.
Element “C1”
Element “B”
Element “A”
Link “C”