## Slide 1: NSI Framework
Uniquely identifying an NSA
John MacAuley

## Slide 2: What is an NSA?
The Network Service Agent (NSA) is a logical software entity that implements the NSI interface as well as the supporting processes to interact with the transport resources and/or middleware to deliver the requested service.

## Slide 3: Statements
A logical NSA entity is identified by a single NSA identifier.
There is a one-to-one mapping between an NSA identifier and a physical network being modeled.
A single NSA identifier cannot map to multiple physical networks.
The requesterNSA and providerNSA elements in the NSI message header is the only mechanism that can be used to uniquely identify the source and target NSA for the message.

## Slide 4: Statements
The messaging layer address (SOAP endpoint) must not be used to uniquely identify an NSA.
A network address must not be used to uniquely identify an NSA.
Multiple logical NSA entities may exist on a single physical server.
A single logical NSA may be implemented across multiple physical servers.
A unique messaging layer address (SOAP endpoint) may exist for each logical NSA function (Discovery Service, Connection Service, and Topology Service).

## Slide 5: NSA Deployment Examples Standard view – Multiple servers
In this example there are multiple logical NSA each on a dedicated server with a dedicated protocol endpoint.
Server
Provider NSA 1
Provider NSA 2
Requester NSA 3
Protocol endpoint
Protocol endpoint
Server

## Slide 6: NSA Deployment Examples Single Server – Multiple NSA – Single Protocol Endpoint
In this example there are multiple logical NSA present on a single server, however, they share a single protocol endpoint.
Server
Provider NSA 1
Provider NSA 2
Requester NSA 3
Single protocol endpoint

## Slide 7: NSA Deployment Examples Single Server – Multiple NSA – Multiple Protocol Endpoint
In this example there are multiple logical NSA present on a single server each with a dedicated protocol endpoint.
Server
Provider NSA 1
Provider NSA 2
Requester NSA 3
Protocol endpoint
Protocol endpoint

## Slide 8: NSA Deployment Examples Single Server – Single NSA – Multiple Protocol Endpoint
In this example there is a single logical NSA present on a single server with a dedicated protocol endpoint for each supported service.
Server
Provider NSA 1
Requester NSA 3
Discovery Protocol endpoint
Topology Protocol endpoint
Connection Protocol endpoint

## Slide 9: NSA Deployment Examples Multiple Server – Single NSA – Multiple Protocol Endpoint
In this example there is a single logical NSA with individual functions deployed on a dedicated server.
Server
Provider NSA 1
(Discovery)
Provider NSA 1
(Connection)
Requester NSA 3
Protocol endpoint
Protocol endpoint
Server