## Slide 1: Motivation for Changes in RSM (CSv2.1)
The current CSv2.0 RSM does not allow the AG to reflect that a uPA has transitioned to a ReserveTimeout state
  When both the AG and uPA are in the ReserveHeld state and a uPA expires the resource hold, only the uPA will transition to the ReserveTimeout state
  The rsvTimeout.nt notification generated by the timed-out uPA is passed up the tree to the uRA, but does not alter the state of any AG along the upstream control-plane path
  Queries (especially by 3rd party applications) to any AG along control-plane path will see the reservation state in ReserveHeld

## Slide 2: RSM: Reservation State Machine (CS v2.1)
Reserve
Held
Reserve
Checking
Reserve
Failed
<rsv.fl
<rsv.fl
<rsv.cf
<rsv.cf
<rsvcommit.cf
<rsvcommit.cf
>rsv.rq
>rsv.rq
>rsvcommit.rq
>rsvcommit.rq
Reserve
Committing
Transitional States
Initial State
Stable States
Reserve
Aborting
Reserve
Timeout
(reserve_timeout)
<rsvTimeout.nt
<rsvTimeout.nt
>rsvabort.rq
>rsvabort.rq
>rsvabort.rq
>rsvabort.rq
<rsvabort.cf
<rsvabort.cf
>rsvabort.rq
>rsvabort.rq
Reserve
Start
Input event+
Input message+
Output message
Output event
+Either Input event or Input message can trigger output (logical disjunction)
“>” = downstream message
“<“ = upstream message
>rsvcommit.rq
>rsvcommit.rq
<rsvcommit.fl
<rsvcommit.fl
Changes from CS v2.0
AG can now transition to ReserveTimeout on receipt of rsvTimeout.nt notification from uPA
Notes:
1a: uPA transits this path if the resource requested is available
1b: uPA transits this path if the resource requested is not available
2a: uPA transits this path if no timeout has occurred
2b: uPA transits this path if a timeout has occurred
3: reserve_timeout event can only occur on uPA
2b
2a
1a
1b
3

## Slide 3: PSM: Provisioning Lifecycle
Releasing
Provisioning
>prov.rq
>prov.rq
>rel.rq
>rel.rq
<rel.cf
<rel.cf
<prov.cf
<prov.cf
Scheduled
Provisioned
Transitional States
Initial State
Stable States
No changes from CS v2.0
Input event+
Input message+
Output message
Output event
+Either Input event or Input message can trigger output (logical disjunction)
“>” = downstream message
“<“ = upstream message

## Slide 4: LSM: Termination Sequence
Stable States
Transitional State
Final State
Terminated
Terminating
Created
>term.rq
>term.rq
<term.cf
<term.cf
Failed
<forcedEnd.nt
<forcedEnd.nt
>term.rq
>term.rq
Passed
EndTime
endTimeEvent
>term.rq
>term.rq
Initial State
Changes from CS v2.0
forceEnd changed to forceEnd.nt
Input event+
Input message+
Output message
Output event
+Either Input event or Input message can trigger output (logical disjunction)
“>” = downstream message
“<“ = upstream message