## Slide 1: OGF NSI CS Protocol State Machine
Converged single view
June 22, 2011

## Slide 2: Overview
This slide package provides a consolidated state machine for the NSI connection services protocol
  Combines aspects of the Ultimate Provider, Ultimate Requestor, Aggregator, and Behavioral state machines for an NSA.
After extensive discussions it was decided that combining all four state machines provided a clearer view of message flow and behaviors within the protocol
  Messages not needed by the implementing NSA can be ignored (i.e. the Ultimate Requestor can ignore messages up to parent NSA).
  The Ultimate Provider can use internal events or child messages to model NRM interactions.

## Slide 3: State Machine Notation
Transition notation
  black: an internal event representing either a timer or result of an operation within the NSI protocol.
  red : an input event which is an NSI message
  blue: an output event which is a NSI message
Message direction
  >: Downstream input/output
  <: Upstream input/output
Message notation
  rsv: reserve, prov: provision, rel: release, cncl: cancel, fcd_end: forced end
  .rq : request, .cf: confirm
Message interaction with children NSA
  *: for input, receive from all children and for output, send to all children
  &: received one or more of this message
  #: received one or more .fl messages from children, and received .cf messages from other children (if exist)
Input Event
Input Message
Output Message
Output Event

## Slide 4: Protocol Events
*_ok: successful operation resulting in a positive state transition and generation of a confirmation message.
*_ng: a negative result on the operation resulting in a negative state transition and generation of a failed response.
reserve_ok: reservation of resources within local NRM and child NSA was completed successfully for the specified schedule criteria.
reservation_ng: reservation of resources failed within one or more of the local NRM or child NSA.
provision_ok: provisioning of resources within local NRM and child NSA was completed successfully for the reservation.
provision_ng: provisioning of resources failed within one or more of the local NRM components or child NSA.
provision: output event indicating that provisioning of resources relating to the reservation should begin.

## Slide 5: Protocol Events
release_ok: release of resources within the local NRM and child NSA was completed successfully for the reservation.
release_ng: release of resources failed within one or more of the local NRM components or child NSA.
release: : output event indicating resources allocated to the reservation are released.
cancel_ok: cancel of a reservation within local NRM components and child NSA was completed successfully for the reservation.
cancel_ng: cancel of a reservation failed within one or more of the local NRM components or child NSA.
cancel: output event indicating resources allocated to the reservation are released and schedule is terminated.
start_time: start time of the reservation.
end_time: end time of the reservation.
forced_end: resources allocated to the schedule were (administratively) released by the local NRM outside of the NSI protocol.

## Slide 6: Combined State Diagram with events and NSI messages
Reserving
Scheduled
Provisioned
Provisioning
Releasing
Initial
Terminated
Any
state
Canceling
Cleaning
Reserved
Auto
Provision
>rsv.rq
>rsv.rq*
(reserve)
(reserve_ok)
<rsv.cf*
<rsv.cf
(reservation_ng)
<rsv.fl&
<rsv.fl, >cncl.rq*
>cncl.rq
>cncl.rq*
(release)(cancel)
>prov.rq
>prov.rq*
(start_time)
(start_time)
(provision)
>prov.rq
>prov.rq*
(provision)
(provision_ok)
<prov.cf*
<prov.cf
(provision_ng)
<prov.fl#
<prov.fl
>rel.rq
>rel.rq*
(release)
(release_ok)
<rel.cf*
<rel.cf
(release_ng)
<rel.fl#
<rel.fl
(forced_end)
<fcd_end&
<fcd_end, >cncl.rq*
(release) (cancel)
(end_time)
(release) (cancel)
(cancel_ok)
<cncl.cf*
(cancel_ok)
<cncl.cf*
<cncl.cf
>prov.rq
<prov.fl
>rel.rq
<rel.fl
>cncl.rq
<cncl.fl
<prov.cf*
<prov.cf
<rel.cf*
<rel.cf
<cncl.cf*
<cncl.cf
<prov.fl#
<prov.fl
<rel.fl#
<rel.fl