## Slide 1: Network Services Interface
Modify operation proposal

## Slide 2: What is the problem?
NSI needs the ability to modify an existing connection reservation.
Three key features:
  1. Modification of schedule endTime.
  2. Modification of reservation bandwidth.
  3. Hitless modification of provisioned service.
Notes:
  Modify request should succeed if the existing reservation path can support the request, and fail it otherwise.
  If the existing path can be expanded to allow more bandwidth, or the endTime can be modified without impacting any other schedules, then we should allow it.
  NOT requesting rerouting, bridge and switch, or any other advanced capabilities.

## Slide 3: Use Case: Cloud Bypass
SARA has implemented an automatic cloud bypass solution used to reroute huge data transfers between GRID sites
How it works
  Monitor uplink of a switch looking for certain traffic patterns
  When traffic match encountered setup a dynamic lightpath between source and destination belonging to that specific traffic pattern
  Reroute matching traffic over the dynamic path
Why modification?
  Do not know how long the traffic will last, or if the traffic will increase or decrease over time
  Do not want to make a reservation for a week at full capacity of the port
  Make a reservation for an hour and check the traffic pattern again 5 minutes before end of reservation, changing capacity or duration if needed

## Slide 4: Modify State Machine – Fire and Pray
Allocating
Committed
>modify.rq
>modify.rq
(allocate)
(allocate_cf)
<modify.cf
<modify.cf
Reservation A’
Initial
Reservation A
(allocate_fl)
<modify.fl
<modify.fl
(pooched)
Operations
modify
Issues
In a tree model a child NSA may fail to perform the modify, however, all other children NSA may have committed the change. We now have a reservation within the network that is in an inconsistent state. Backing out the change would be extremely complex, as the requesting NSA would need to remember the original reservation parameters and re-issue them down the tree with another modify to try and restore consistency.

## Slide 5: How do we fix this consistency issue?
In our distributed environment we will need to make modify a two-phase commit operation
In the first phase…
  A modifyRequest is issued down the tree to check the feasibility of the desired reservation modification, and to reserve any additional network resources associated with the request
  A modifyConfirm message will be sent back to the requester if the requested modification is possible, and as an acknowledgment to successfully securing any additional network resources
  A modifyFailed message will be sent back to the requester if the requested modification is not possible
  At successful completion of the first phase the original reservation is still preserved, however, pre-allocation of any additional resources associated with the modify has been completed for all participating NSA
  If the first phase ends in failure then the original reservation is preserved

## Slide 6: Phase Two
In the second phase…
  A modifyCommitRequest is issued down the tree to commit the reservation modification
  A modifyCommitConfirm message will be sent back to the requester if the requested modification commit is successful, and the modified schedule is in effect
  A modifyCommitFailed message will be sent back to the requester if the modification commit is not possible (would not be due to lack of resources)
  At successful completion of the second phase the original reservation has been replaced with the modified version
  If the second phase ends in failure then a critical error has occurred and the reservation is in an indeterminate state within the network

## Slide 7: Commit Timeout
To avoid leakage of uncommitted modification resources we will need to implement a commit timeout
If a corresponding modifyCommitRequest is not received within 5 minutes of a modifyConfirmed message then any pending resources against that reservation should be released
The original reservation is preserved

## Slide 8: Modify State Machine – Two Phase**
Allocating
Committed
Allocated
Committing
>modify.rq
>modify.rq
(allocate)
(allocate_cf)
<modify.cf
<modify.cf
>modifyCommit.rq
>modifyCommit.rq
(commit)
(commit_cf)
<modifyCommit.cf
<modifyCommit.cf
Reservation A’
(commit_timeout)
(deallocate)
Initial
Reservation A
(allocate_fl)
<modify.fl
<modify.fl,
(deallocate)
Operations
modify
modifyCommit
** Use timeout to clean up after failures
(commit_fl)
<modifyCommit.fl
<modifyCommit.fl
(pooched)

## Slide 9: Modify State Machine – Two Phase
Allocating
Committed
Allocated
Committing
>modify.rq
>modify.rq
(allocate)
(allocate_cf)
<modify.cf
<modify.cf
>modifyCommit.rq
>modifyCommit.rq
(commit)
(commit_fl)
<modifyCommit.fl
<modifyCommit.fl, >modifyCancel.rq
(pooched)
(commit_cf)
<modifyCommit.cf
<modifyCommit.cf
Reservation A’
(commit_timeout)
(deallocate)
Initial
Reservation A
Cleaning
(allocate_fl)
<modify.fl
<modify.fl, >modifyCancel.rq
(deallocate)
(deallocate_cf)
<modifyCancel.cf <modifyCancel.fl
Operations
modify
modifyCommit
modifyCancel
Do we really need the modifyCancel? Will this force all NSA to restore the previous reservation values?