## Slide 1: NSI CS Protocol State Machine Message Handling
OGF 37

## Slide 2: Coordinator and Message Transport Layer (MTL)
Coor is a part of NSI stack, and uses MTL to send/receive messages
Coor is primarily responsible for keeping track of messaging state, e.g.
  Who was the message sent to
  Was the message received (i.e. ack’ed or MTL timeout)
  Who has not replied to the message (e.g. *.cf, *.fl, etc)
MTL is primarily responsible for sending and receiving messages, and notifying Coor if the message was received, or if a (MTL) timeout occurs
MTL interface (to Coor) has 2 simple operations:
  Send: waits for ack to be returned by destination MTL, or timeout happens. Timeout value is implementation dependent. NB: The MTL may be implemented to retry sending messages, but this is opaque to the Coor
  Receive: a thread in Coor is invoked when a message is received
NSA
NSI Stack
Message Transport Layer
Coordinator

## Slide 3
NSA
(ultimate) Provider Agent
Message Transport Layer
Network Resource Manager
Coordinator
NSA
(ultimate) Requester Agent
Message Transport Layer
Coordinator
NSA
(ultimate) Provider Agent
Message Transport Layer
Aggregator Agent
Message Transport Layer
Network Resource Manager
Coordinator
Coordinator
NSA
Aggregator Agent
Message Transport Layer
Coordinator
NSA
(ultimate) Provider Agent
Message Transport Layer
Network Resource Manager
Coordinator
Request Workflow Tree Example
Dual function NSA (e.g. AG and uPA)

## Slide 4: Message ack, reply and timeouts
Ack is sent by MTL for each message
  If ack is not returned in a certain period of time, MTL timeout occurs
Reply is sent by Coor (via MTL) and is either confirm, fail or not_applicable
  Coor can timeout if expected reply is not received from a child
: MTL timeout may happen
: Coor timeout may happen
NSA
Provider Agent
MH
MTL
Coor
NSA
Requester Agent
MTL
Coor
message
ack
request
return
return
reply
message
reply
ack
notification
message
ack
return
notification
request

## Slide 5: Timeouts
Message transport layer (MTL) timeout
  Underlying MTL (http/tcp) initiates a MTL timeout
  Happens when an ack is not returned for a message.
Coordinator timeout
  Coor can timeout if a reply message is not returned in a certain period of time
Coor notifies both MTL and Coor timeouts to the parent RA
When a MTL/Coor timeout is notified, uRA can either retry or terminate the connection.
  Retry is requested by NSI_messageRetry.rq, which has the original request message's id (correlation id) as a parameter
  Coor keeps not-yet-replied requests in a table, so that it can re-send the request.

## Slide 6: Notifications: Activation related
There are no activateComplete.nt nor deactivateComplete.nt
A general error message is used to notify following events. Those error are sent up the tree to uRA immediately
  activateFailed: Activation failed at the time when uPA should activate its data plane
  deactivateFailed: Deactivation failed at the time when uPA should deactivate its data plane
  dataplaneError: Data plane is deactivate when deactivation is not expected. The error is recoverable.
  forcedEnd: Something unrecoverable is happened in uPA/NRM

## Slide 7: Notifications: modify timeout and MTL failure
NSI_modifyTimeout.nt
NSI_genericEvent.nt
  Message delivery failure will be notified by this message (to be defined)
When a MTL/Coor timeout is notified, uRA can either retry or terminate the connection.
  Retry is requested by NSI_messageRetry.rq, which has the original request message's id (correlation id) as a parameter

## Slide 8: Data plane activation
Data plane should be activated if the PSM is in “Provisioned” state AND start_time < current_time < end_time
Activation is done at the timing of following events (if the above condition is met), using the latest reservation information
  PSM transits to “Provisioned”
  At the start_time
  Reservation is updated (by commit of modify)
  Data plane is recovered from an error
Data plane activation/deactivation are notified by DataPlaneStateChange.nt notification messages.
Errors are notified by a generic error message

## Slide 9: DataPlaneStateChage.nt (1)
PA and aggregator has DataPlaneStatus information
  (Boolean) Active: True if data plane is active. For an aggregator, this flag is true when data plane is activated in all participating children
  (Int) Version: For a uPA, current (latest) reservation version number. For an aggregator, the largest version number of the participating children. This field is valid when Active is true.
  (Boolean) VersionConsistent: Always true for uPA. For an aggregator, If version numbers of all children are the same, This flag is true. This field is valid when Active is true.
When a valid filed of DataPlaneStatus is changed, DataPlaneStatusChange.nt is sent up.
Active
Version
VersionConsistent
DataPlaneStatus

## Slide 10: DataPlaneStateChange.nt(2)
An aggregator keeps an array of statuses of its children, ChildrenDataPlaneStatus[1..n]
Aggregator’s DataPlaneStatus is determined by the following rule
if all of ChildrenDataPlaneStatus[1..n].Active are true
then
{
DataPlaneStatus.Active = true
DataPlaneStatus.Version =
maximum_of(ChildrenDataPlaneStatus[1..n].Version)
If all ChildrenDataPlaneStatus[1..n].Version are the same, and all
of ChildrenDataPlaneStatus[1..n].VersionCosistent are true
then DataPlaneStatus.VersionConsistent = true
else DataPlaneStatus.VersionConsistent = false
}
Active
Ver.
VC
ChildrenDataPlaneStatus
Active
Ver.
VC
DataPlaneStatus
Active
Ver.
VC
Active
Ver.
VC
Child 1
Child 2
Child n

## Slide 11: Information tracked by Coordinator
1Conn_ID, A-Z STPs, Parameters
1.1Corr_ID, Status
1.2Corr_ID, Status
1.1NSA, Conn_ID, A-Z STPs, Parameters, RSM, PSM, LSM, Data_Plane
1.2NSA, Conn_ID, A-Z STPs, Parameters, RSM, PSM, LSM, Data_Plane
1.nNSA, Conn_ID, A-Z STPs, Parameters, RSM, PSM, LSM, Data_Plane
1.1.1Corr_ID, Status
1.1.2Corr_ID, Status
1.1.nCorr_ID, Status
1.2.1Corr_ID, Status
1.2.2Corr_ID, Status
1.2.nCorr_ID, Status
List of Connection Reservations
connection_list(Conn_ID)
List of children NSAs associated with a Connection Reservation
connection_segment_list(Conn_ID, NSA)
A connection reservation may be broken down into several smaller segment requests to other (children) NSAs
Information generated per Reservation (Connection)
Information generated per NSI Request (Message)
List of (summary) NSI Requests associated with a Connection Request
request_list(Conn_ID, Corr_ID)
List of child NSA NSI Requests associated with a (summary) NSI Request
request_segment_list(Conn_ID, NSA, Corr_ID)
A connection reservation will consist of one or more NSI Requests
An NSI request may result in several distinct child NSA NSI Requests
Each NSA segment NSI Request is associated to the corresponding child NSA Connection Reservation