## Slide 1
Network B
Network C
Network D
Network A
STP
B.A
STP
A.C
STP
B.D
STP
D.C
STP
B.C
STP
C.A
STP
D.B
STP
C.D
STP
C.B
Problem statement: EROs can be ambiguous with implicit bi-directional STPs
STP
A.1
STP
A.B
STP
D.1
Terminating* STP
Intermediate* STP
Request Valid Path Solutions
A-Point = A.1 Path 1: A.1, A.B, B.A, B.C, C.B, C.D, D.C, D.1
Z-Point = D.1 Path 2: A.1, A.C, C.A, C.B, B.C, B.D, D.B, D.1
ERO = A.1, B.C, D.1
* As per request instance
Path 1
Path 2
Selected STP (B.C) in ERO

## Slide 2
Network B
Network C
Network D
Network A
STP
B.A
STP
A.C
STP
B.D
STP
D.C
STP
B.C
STP
C.A
STP
D.B
STP
C.D
Solution Option 1: Use Dual-STPs/Full-SDPs for EROs
STP
A.1
STP
A.B
STP
D.1
Terminating* STP
Intermediate* STP
* As per request instance
Path 1
Request Valid Path Solutions
A-Point = A.1 Path 1: A.1, A.B, B.A, B.C, C.B, C.D, D.C, D.1
Z-Point = D.1
ERO = A.1, B.C, C.B, D.1
Selected Dual-STP/Full-SDP (B.C, C.B) in ERO
STP
C.B

## Slide 3
Network B
Network C
Network D
Network A
STP
B.A
STP
A.C
STP
B.D
STP
D.C
STP
B.C
STP
C.A
STP
D.B
STP
C.D
Solution Option 2: Add Polarity/Orientation to STPs
STP
A.1
STP
A.B
STP
D.1
Terminating* STP
Intermediate* STP
* As per request instance
Path 1
Selected STP with orientation (B.C_out) in ERO
STP
C.B
Request Valid Path Solutions
A-Point = A.1_in Path 1: A.1_in, A.B_out, B.A_in, B.C_out, C.B_in,
Z-Point = D.1_out C.D_out, D.C_in, D.1_out
ERO = A.1_in, B.C_out, D.1_out
These STPs are redundant. If A.Bout is explicitly specified, then B.Ain is implied.

## Slide 4
Network B
Network C
Network D
Network A
STP
B.A
STP
A.C
STP
B.D
STP
D.C
STP
B.C
STP
C.A
STP
D.B
STP
C.D
Solution Option 3: Use Directional+ SDPs
(Directed Demarcation Point (DDP)) for EROs
STP
A.1
STP
A.B
STP
D.1
Terminating* STP
Intermediate* STP
+ Direction is relative to source/destination STP * As per request instance
Path 1
Selected DDP (SrcWard:B.C, DstWard:C.B) in ERO
STP
C.B
Request Valid Path Solutions
A-Point = A.1 Path 1: A.1, DDP(SrcWard:A.B, DstWard:B.A),
Z-Point = D.1 DDP(SrcWard:B.C, DstWard:C.B),
ERO = A.1, DDP(SrcWard:C.D, DstWard:D.C), D.1
DDP(SrcWard:B.C, DstWard:C.B),
D.1

## Slide 5
Network B
Network A
Basic Path Ambiguity Problem:
STP
A.1
Terminating* STP
Intermediate* STP
STP
A.2
STP
B.1
STP
B.2
Network B
Network A
STP
A.1
STP
A.2
STP
B.1
STP
B.2
Path 1
Network B
Network A
STP
A.1
STP
A.2
STP
B.1
STP
B.2
Path 2
Request Valid Path Solutions
A-Point = A.1 Path 1: A.1, B.1, B.2
Z-Point = B.2 Path 2: A.1, A.2, B.2
Path 1 and Path 2 are not compatible! Their respective ingress and egress points reside in different networks!
Since there are no intermediate SDPs, EROs are irrelevant to resolving path ambiguity.
The ambiguity exists for A.1>A.2 as well. And B.1>B.2. And B.1>A.2.
Only one reservation segment is correct. The other will not work.

## Slide 6
Network B
Network A
JS proposal: Oriented STPs:
A.1out
B.1in
Network B
Network A
STP
A.1
STP
A.2
STP
B.1
STP
B.2
Path 1
Network B
Network A
STP
A.1
STP
A.2
STP
B.1
STP
B.2
Path 2
Request Only one Valid Path Solution
A-Point = A.1out Path 1: A.1out, B.1in, B.2out
Z-Point = B.2out
STPs are oriented in topology DB, naming (“in” or “out” is simple human convenience)
Path finders learn orientation as they traverse the topology. E.g. A.1out has only one transit possibility.
Thus A.1out>B.2out is equivalent to B.1in>B.1out.
Existing Reservation construct is unchanged – STPs are referenced as before.
Still allows for EROs – simple list of STPs. Their orientation problem is resolved as well.
Thus we can still use A.1out>B.2out to indicate both net A and B are contacted.
Further, this allows unidirectional connections to be built without changing the protocol.
A.1in
B.1out
A.2out
B.2in
A.2in
B.2out